Full color Asynchronous controller Parameter

----------HD-C30

## Led display controller functions

HD-C30 is Asynchronous led display controller, and working no need PC. Playing high definition programs .like video, image, animation, text, temperature, office file etc. The system include two parts HD-C30 controller and software called HD Player.

Usually one screen with 1pcs HD-C30+1PCS HUB, if the screen is bigger, for best result, user can add R500/R501 cascade connection. So HD-C30 is Full color Asynchronous cascaded controller

- Device list

| types | model | Main function |
| --- | --- | --- |
| Full color asynchronous cascade controller | HD-C30 | Asynchronous core controller, with 4Gmemory function, and connected display Itself also can be used as 1PCS receiving card |
| Receiving card | R500/R501 | Connected screen, show the program on LED screen |
| Controller software | HD Player | Setting screen parameter, edit and send program |
| Accessories |  | HUB board, cable , U-disk |

3 Model Selection Reference

| Model | Control range(width* height) | sub model |
| --- | --- | --- |
| HD-C30 | 640（width）*480（height）; 1024（width）*300（height）; 600（width）*512（height）; | HD-C30F（WIFI） HD-C30W（3G） HD-C30G（4G） |
| R500 | Recommend :256（width）*128（height） |  |
| R501 | Recommend :256（width）*192（height） |  |

Notice: If Display less than 256W*128H, Suggest 1PCS HD-C30+1PCS HUB

If Display 640W*480H, Suggest 1PCS HD-C30 +4PCS R500 or 3PCS R501

If Display 1024W*300H, Suggest 1PCS HD-C30 +4PCS R500 or 4PCS R501

If Display 600W*512H, Suggest 1PCS HD-C30 +4PCS R500 or 3PCS R501

## 4 .Application place

## Control card can connect with router, internet cascaded management as bellow:

## Picture 4-1 managing several screen through Internet

2) Control card can connect with computer directly, showing as bellow:

Picture 4-2   only one screen and control by Network cable directly

# Notice: Each screen just need 1PCS C30 card, and the number of receiving card depend on screen size.

# Updated program can by Network cable directly, also updated via U-disk and moving hard disk drive.

# 5. Advantage than old version HD-C1/HD-C3

# 1) Price cheaper than C3

# 2) Showing effects better and refresh higher

# 3) Opening display time shorted to 25seconds

# 4）Also can cascaded and then good effects

# Also support 1 cabinet 1 controller

# 5) Add functions of SWF flash, neon, animation character, internet weather report

# 6) Flashed memory: Changed to 4GB

# 7) Have 3G/4G and WIFI version controller

6. Details Parameter

| Module types | Compatible indoor and outdoor, full color and single/dual color module; Support virtual module; Support PWM chips such as MBI5041/5042、MBI5050、MY9221、MY9268. |
| --- | --- |
| Scanning mode | Support static scan and 1/32 scan randomly |
| Control range | 640（width）*480（height）; 1024（width）*300（height）; 600（width）*512（height）; |
| Single receiving card pixels control range | Suggest HD- R500: 256（width）*128（height） HD-R501: 256（width）*192（height） |
| Gray level | Support 0-65536 adjustable |
| Program update | Updated by PC, LAN, Internet, U-disk, or mobile hard disk drive |
| Showing functions | video, pictures, animated Gif, text, office document, clock, timer etc Support remote control, temperature, humidity, brightness expansion function |
| Video function | Support hardware video decoder, sending directly, and without transfer code waiting. Support format AVI、WMV、RMVB、MP4、3GP、ASF、MPG、FLV、F4V、MKV、MOV、DAT、VOB、TRP、TS、WEBM |
| Picture format | Support BMP、GIF、JPG、JPEG、PNG、PBM、PGM、PPM、XPM、XBM etc |
| Text | Support for text editing, picture insertion and support word、txt、rtf、html direct importing. |
| Document | Support Office2007 such as DOC、DOCX、XLSX、XLS、PPT、PPTX document format. |
| Clock | Support analog clock, digital clock, A variety of dial clock |
| Audio output | Standard dual channel stereo output |
| Memory capacity | On board Flash 4GB Allows users to use U-disk memory expansion |
| Communication type | 100M network Port RJ45, Internet, or LAN |
| Operating temperature | -20℃-80℃ |
| Port | IN: 5V power supply terminal X1, 10/100M RJ45 x1，USB 2.0 x1，The screen test button X1 OUT:1000M RJ45 x1，dual stereo: AUDIO x1 , 2 of 50 PIN |
| Working voltage | 4.5V~5.5V |
| Software | HDPlayer |

7. Port Instruction

- HD-C30 Port  Instruction:

①USB port, connect USB device, such as: U-disk and mobile hard disk drive

②Input network port, 100M network port, Normal working: orange lamp always on,green lamp flicker.

③Output network port,1000M network port, Normal working: D7 green lamp always on, D8 green lamp flicker.

④ Power interface, 2 pin power terminal connect with 5V power

⑤ Audio output interface, standard dual channel stereo output

⑥Power led-D2 green lamp normal working is always on, running lights-D1green lamp normal working is flicker.

⑦ MINIPCIE connect 3G model or WIFI model (select-able)

⑧1 of 50 pin, connect HUB board, connecting with all kind of cabinet interface through HUB

⑨Display lamp-D7green lamp normal working is flicker

⑩The back SIM card slot, inserted with 3G/4G card for 3G/4G internet solutions

2) 50 pin definition

Support 16 “RGBR” Parallel Data, definition as below:

General Full Color Port 1                         General Full Color Port 2

8, Dimension Chart

- HD-C30 dimension chart as bellow:

Picture 8-1 HD-C30 dimension chart

2) Receiving card dimension chart as below

Picture 8-2 dimension chart R500

Picture 8-3  Dimension Chart R501