# Asynchronous Full-color LED Display Controller HD-D10

# 1.Features：

# ①.Support indoor & outdoor full-color & single/dual color module.

②.Control range Pixel:

192W*128H  384W*64H  512W*48H

③.Support 256 Gray scale.

④.Support Video、Animation、Image、Neon 、 Office file   etc .

⑤.Support U-disk expanding memory, plug and play.

⑥.Plug and play without any network settings.

⑦.Support Internet /3G/4G Clouds management

2.Parameter

| Type | Indoor & outdoor full-color & single/dual color module |
| --- | --- |
| Control range | Pixel: 384(W)*64(H) . longest 512 highest 128 |
| Gray Scale | 256 |
| Video format | AVI、WMV、RMVB、MP4、3GP、ASF、MPG、FLV、F4V、MKV、MOV、DAT、VOB、TRP、TS、WEBMetc. |
| Animation format | SWF、FLV 、GIF |
| Image format | BMP, GIF, JPG, JPEG, PNG, GIF, etc. |
| Text | Text and Image being edited directly. |
| Time | Classic Analog clock, digital clock and various of clock with image background |
| Other function | Neon, animations function; Clockwise/counter-clockwise count; support temperature and humidity; Adaptive brightness adjustment function |
| memory capacity | 256MB Flash, more than 2 hours’ program support. Indefinite expanding of U-disk memory. |
| Communication | U-disk; Via NetworkRJ45 port connected LAN,Internet or 3G/4G to Internet |
| Port | 5V Power x1, 10/100M RJ45 x1, USB 2.0 x1, 4Port of HUB75 |
| software | HDPlayer |

3.Connected ways

①.Controller can be connected to the router ,then into Internet to management

②.Controller can be connected to the computer

③.Updated program: Except use LAN Cable ,also can via U-Disk or Portable Hard-disk

4. HD-D10  Interface explanation

①：USB port，Plug in the U-disk or mobile hard disk，update program；

②：Power terminal to connect 5 v power supply；

③： RJ45 internet access .HD-D10 connected to the computer internet access, router or switch，Normal working state is orange lights on, green lights flashing

④：MINIPCIE,connect 3G module or WIFI module (selectable)；

⑤：4×2*8PIN, HUB75B，connect LED screen；

⑥： SIM card slot，3G/4G SIM card.

5. Definition of HUB port

Support 4 groups HUB75 parallel data are defined as follows:

6. Assembly drawing