# Asynchronous Full-color LED Display Controller HD-D20

# 1.Features：

# ①. Support indoor & outdoor full-color & single/dual color module.

②.Control range Pixel:

192W*128H   384W*64H   512W*48H

③.Support 256 Gray scale.

④.Support Video、Animation、Image、Neon 、 Office file etc .

⑤.Support U-disk expanding memory, plug and play.

⑥.Plug and play without any network settings.

⑦.Support Internet /3G/4G Clouds management

2.Parameter

| Type | Indoor & outdoor full-color & single/dual color module |
| --- | --- |
| Control range | Pixel: 192W*128H 384W*64H 512W*48H |
| Gray Scale | 256 |
| HUB Port | 6 of HUB08 inside |
| Video format | AVI、WMV、RMVB、MP4、3GP、ASF、MPG、FLV、F4V、MKV、MOV、DAT、VOB、TRP、TS、WEBM etc. |
| Animation format | SWF、FLV 、GIF |
| Image format | BMP, GIF, JPG, JPEG, PNG, GIF, etc. |
| Text | Text and Image being edited directly. |
| Time | Classic Analog clock, digital clock and various of clock with image background |
| Other function | Neon, animations function; Clockwise/counter-clockwise count; support temperature and humidity; Adaptive brightness adjustment function |
| memory capacity | 256MB Flash, more than 2 hours’ program support. Indefinite expanding of U-disk memory. |
| Communication | U-disk; Via NetworkRJ45 port connected LAN,Internet or 3G/4G to Internet |
| Port | 5V Power x1, 10/100M RJ45 x1, USB 2.0 x1, 6 Port of HUB75 |
| software | HDPlayer |

3. Connected ways: HD-D10/D20/D30 series same ways

①.Controller can be connected to the router ,then into Internet to management

②.Controller can be connected to the computer

③.Updated program: Except use LAN Cable ,also can via U-Disk or Portable Hard-disk

4. HD-D20 Interface explanation

① USB port，Plug in the U-disk or mobile hard disk，update program；

② RJ45 internet access .HD-D20 connected to the computer internet access, router or switch，Normal working state is orange lights on, green lights flashing

③ Power terminal to connect 5 v power supply；

④ MINIPCIE, connected 3G module or WIFI module (selectable)；

⑤ 6×2*8PIN, HUB08，connect LED screen；

⑥ Running light: Normal working status and the light is Flicker

⑦ Power light: Normal working status and the light is bright

⑧ Display light: Normal working status and the light is Flicker

⑨ SIM card slot，3G/4G SIM card.

5. Definition of HUB port

Support 6 groups HUB08 parallel data are defined as follows:

6. Assembly drawing